## Slide 1
RangeRectQuant
lossy
Encoding
lossless
Decoding
Input X
Backward
feasibility
Forward
selection
Quantized Y
Split
Y = qZ + r
LZMA
encode
LZMA
encode
Z
r
Bitstream
Storage
Merge
LZMA
decode
LZMA
decode
Z
r
Prefix tables
Four-corner
query
Sum / count
Notes: RangeRectQuant method overview. Source: /Users/nathmath/dcc/RangeRectQuant/paper/main.pdf, pages 3–5, and /Users/nathmath/dcc/RangeRectQuant/paper/sections/method.tex.
Source PDF SHA-256: f389eba57b38470ad9d758f5ee078c7fbb4f4f590b59dbf402b7a63923100dae
Gray upper region: the lossy, row-wise backward–forward construction. Gray lower region: ordinary queries after decoding. Hatched regions: lossless coding and decoding of the constructed Y.
B=floor(epsilon/4). q is the positive integer coarse step. U is the physical upper bound. P includes missing samples and designated exact samples.
Z=floor(Y/q), r=Y mod q. Both arrays use 16-bit low-byte/high-byte shuffle and LZMA preset 6. Bit-packed masks use zlib. The file also contains configuration, geospatial metadata, reconstruction digest, and checksum.
Decoding never reruns or reverses the quantizer and needs neither X nor query-specific corrections. The full missing mask enters the valid-count prefix table.
Arrow endpoints are separate native transparent port shapes. Text, rectangles, patterns, arrows and arrowheads are editable. No raster images are embedded.